## Slide 1: Neutron beams for nuclear data measurements
Arnd Junghans Helmholtz-Zentrum Dresden-Rossendorf Germany

## Slide 2: Table of Content
Introduction of the speaker
Neutron sources (Terrestrial and radioisotope sources)
Neutron producing nuclear reactions: Monoenergetic neutrons
Kinematics e.g. 7Li(p,n)7Be
Neutron reference fields: „Big Four“ reactions for neutron production
Neutron generators: D(d,n)3He, T(d,n)4He reactions
Time-of-flight method and neutron sources
Spallation neutron sources using light-ion accelerators
Slowing down of neutrons to produce eV-keV neutrons
Photoneutron sources using electron accelerators

## Slide 3: curriculum vitae Arnd Rudolf Junghans
1987-1994 Student of Physics at Technische Hochschule Darmstadt Diploma thesis „Influence of fission on the fragmentation of relativistic projectiles in peripheral collisions“
1994-1997 PhD Student Technische Universität Darmstadt Dissertation „Investigation of the collectivity of nuclear excitations in the fragmentation of relativistic uranium projectiles“
1998 Postdoc GSI Darmstadt „Studies of production methods of exotic nuclei“
1999-2002 Postdoc + Research Assistant Professor, CENPA, University of Washington, Seattle: 7Be(p,)8B S-factor measurements -> Solar neutrino problem
since 2003 Scientific Staff at Helmholtz-Zentrum Dresden-Rossendorf Group leader „Physics of Transmutation“ Development of a photoneutron source at the superconducting electron acelerator ELBE

## Slide 4: Doktorgesang 1994 (This is twenty years ago)

## Slide 5: CHARMS evening (this is 11 years ago)
Notes: Collaboration for High-Accuracy Experiments on Nuclear Reaction Mechanisms with magnetic Spectrometers

## Slide 6: Neutron sources
Neutron sources in nature: Neutrons can be formed in nuclear reactions of high-energetic cosmic particles in the upper atmosphere. The flux is inverserly proportional to the solar activity (high solar activity deformes the earth‘s magnetic field) and strongly dependend on the geographical latitude and altitude.
G. Heusser, Low-radioactivity background techniques
Gordon et. al. IEEE TNS 51 (2006) 3427
Thermal peak
Evaporation
peak
High energy
peak
Resonances
from N,O
due to
MCNP sim.
Setup:
Extended range Bonner spheres
14 different size PE moderators
with 3He proportional counters

## Slide 7: Neutron sources
Terrestrial sources: Fission neutrons from spontaneous fission of heavy nuclei Spontaneous fission has been observed on thorium and uranium (and heavier actinides that are not primordial)
Artificial neutron sources: 1. Radioisotope sources based on (,n) reactions, e.g. (Po,Be), (Am,Be) (Cm,13C) or spontaneous fission, e.g. 252Cf (sf) 2. Photoneutron sources 2H(,n)H, 9Be(,n) 3. Accelerator based sources, e.g. (d,n) (p,n) reactions on light nuclei 4. Nuclear reactors (fission neutrons + moderation)
5. Spallation neutron sources
nuclide | f (a-1)
235U | 1.98*10-18
238U | 7.03*10-17
232Th | <6.9*10-22

## Slide 8: Radioisotope sources
(,n) reactions on light nuclei with positive Q-value: e.g. Be, B 9Be(,n)12C Q=5.71 MeV, En = 0 .. 13 MeV
-emitter mixed with Be-powder
complicated neutron energy spectrum, neutron intensity also dependent on purity of the -emitter
background from high-energy gamma emission
13C(,n) is also the main source of neutrons in the astrophyiscal s-process
-delayed neutron emission. e.g. 87Br (t1/2 = 55.7 s)  87Kr* + - 87Kr*  86Kr + n not a practicable neutron source but important for reactor criticality control

## Slide 9: Neutron source: 241Am: 9Be(,n)12C
Content: Mixture of -Emitter M and Beryllium
as a fine powder or as alloy or Actinide-Boride
Yield ca. 10-4 n/-decay
(Most -particles are stopped without causing
a nuclear reaction.)
Lorch, Int. Jour. Appl. Rad. Iso. 24 (1973) 585
complex neutron spectrum :
depending on the individual source.
typically: 5 g Be
0.37 g 241AmO2 = 1 Ci

## Slide 10: Neutron source: 241Am: 9Be(,n)12C
Transitions to discrete states from CN decay
13C*  12C*
neutron spectrum from a thin target shows these transitions
e.g.transition to the 4.44 MeV state in 12C:
En = E + Q – E*(12C) – Erecoil(12C)
= 7.78 MeV + 5.7 MeV – 4.44 MeV – 0.588 MeV = 8.453 MeV
INDC-NDS-0114(1980)
Proton recoils in stilbene
scintillators

## Slide 11: Am-Be source spectrum
Non g.s. neutron groups also lead to
high energy -ray emission

## Slide 12: 252Cf spontaneous fission neutron spectrum
252Cf T1/2 = 2.65 a,  = 96.908%, SF 3.092% <n> = 3.756 +- 0.005; 0.116 n/Bq; 2.30*106 n/(s g)
Fission neutron spectrum has a approximately maxwellian distribution with T = 1.42 MeV
252Cf is a very strong radioisotope neutron source
Also emitted are 10 prompt -rays per fission.

## Slide 13: Photoneutron sources with radioisotopes
2H(,n)H, Q= -2.226 MeV 9Be(,n) Q = -1.666 MeV
negative Q-value  high energetic -emitter is required
m – neutron mass, M residual nucleus mass
monoenergetic -emitter can deliver a quasimonoenergetic neutron source
dependence of En on emission angle 
low neutron yield ca. 10-5 – 10-6 n/ 
high energetic -emitters are mostly short lived  production in reactor or accelerator facility, e.g. 24Na t1/2 = 15 h, 88Y t1/2 = 107 d

## Slide 14: Neutron producing nuclear reactions
In two-body reactions monoenergetic neutrons can be produced, e.g. DT-reaction: 3H(2H,n)4He, Q = 17.16 MeV
Kinematics determines the angular distribution and energy spectrum
The yield (neutrons /primary particles) is determined by the differential cross section
Realistic yield determination by integration over the target thickness and angular range (slowing down of the beam in the target material)

## Slide 15: Relativistic two body kinematics
projectile hits target after the reaction: ejectile (e.g. a neutron) , recoiling nucleus
momentum of projectile and target in the center of mass frame
momentum of ejectile and recoil in the c.m. frame
For the initial system
with
In the c. m. frame
The four momentum squared
is lorentz-invariant. (invariant mass)

## Slide 16: Relativistic two body kinematics
Lorentz-transformation formulated using the rapidity Y
Boost from lab. to c.m. system
c.m. momentum of the target is
With
Rapidity of the c.m. system
„Rapidité“ Jacques Tati, Jour de Fête, 1949

## Slide 17: Relativistic two body kinematics
Energy/momenta of the reaction products calculated using the invariant mass and the rapidity of the c.m. system
Lorentz transformation with c.m rapidity
transversal momenta are lorentz-invariant

## Slide 18: Lab. momenta as function of the lab. angles:
1. Isolate the c.m. angle terms and square them 2. sum both momentum projections cancels  quadratic equation for
Two solutions of !
For endothermic reactions MeV Forward threshold (minimum kinetic energy for the reaction to occur) derived from
If the ejectile is slower than the c.m. velocity is a double-valued function of the lab angle . Equivalent: is a double-valued function of
up to the back threshold

## Slide 19: 7Li(p,n)7Be : neutron energy vs. angle
MeV ; MeV ; MeV
1.8806 MeV
threshold
1.89
1.90
1.91
1.92
1.93
1.94
Ep= 1.95 MeV
Lab. neutron emission angle
Lab. neutron energy
Two neutron energy
groups below

## Slide 20: 7Li(p,n)7Be: neutron angle vs. c.m. angle
Below MeV the c.m. emission angle is a double-valued function of the lab. emission angle
1.8806 MeV
threshold
1.89
1.90
1.91
1.92
1.93
1.94
Ep= 1.95 MeV
c.m. neutron emission angle
Lab. neutron emission angle

## Slide 21: 7Li(p,n)7Be : recoil energy vs. angle
1.8806 MeV
threshold
1.89
1.90
1.91
1.92
1.93
1.94
Ep= 1.95 MeV
Two recoil energy
groups

## Slide 22: 7Li(p,n)7Be : recoil angle vs. c.m. angle
1.8806 MeV
threshold
1.89
1.90
1.91
1.92
1.93
1.94
Ep= 1.95 MeV
The c.m. emission angle is a double-valued function of the lab recoil angle

## Slide 23: Conversion from center of mass to laboratory
 Emission angle, e.g. ;
Jacobian matrix for conversion from c.m. to lab system:
For the recoil substitute :

## Slide 24: Neutron Yield
Neutron rate emitted into solid angle by a layer of a thick target by impinging projectiles with rate Np is the atomic density of the target
Through reaction kinematics the projectile energy is related to the energy of the neutron emitted into the solid angle . decreases due to the electronic energy loss in the target material.
The differential neutron spectrum is
Yield Y obtained by integration over the projectile energy
linear stopping power, solid angle element ratio c.m to laborator system, kinematic factor

## Slide 25: Real source yield
Neutron yield depends on target thickness and purity: Energy loss of the beam in the neutron producing target layer  beam heating of the target Thermal motion of target atoms e.g. in gaseous targets
 neutron energy spread
Neutron scattering in target materials, backings, windows
Opening angle and source and detector counting geometry
Kinematic focussing for reactions in inverse kinematics
Monte Carlo neutron transport simulation to describe the neutron spectrum
Time correlated associated particle method  neutron yield measured independent from (Lecture by Ralf Nolte)

## Slide 26: Differential cross sections: 7Li(p,n)7Be; 7Li(p,n)7Be*(429 keV)
7Li(p,n)7Be:
very steep rise
close to threshold
Pronounced resonances:
Ep = 2.25 and 4.9 MeV
resonances are difficult
To predict  cross section measurements
H. Liskien, A. Paulsen Atomic Data Nuclear Data Tables 15 (1975) 57

## Slide 27: Energy range for neutron production
„Monoenergetic“ neutrons from reactions with only one neutron group
„Quasi-monoenergetic“ neutrons from reactions with a second group of neutrons from reactions to excited states of the recoil or nuclear break up
Example: 7Li(p,n)7Be
Energy levels of light nuclei, see http://www.tunl.duke.edu/nucldata/index.shtml
Monoenergetic neutrons from Ep =1.920 MeV – 2.371 MeV En = 121 keV – 649 keV
Reaction | 7Be* Exc. Energy (MeV) | Q-value (MeV) | Threshold (MeV)
7Li(p,n)7Be | 0 | -1.644 | 1.881 forward 1.920 backward
7Li(p,n)7Be* | 0.429 | -2.073 | 2.371 forward 2.421 backward
7Li(p,n3He)4He | break-up | -3.229 | 3.692
7Li(p,n)7Be** | 4.57 | -6.214 | -7.110 forward -7.260 backward

## Slide 28: Neutron production in inverse kinematics
light-ion beam required with higher energy (beam heating) e.g. 1H(7Li,n)7Be Geben Sie hier eine Formel ein.
M. Lebois et al. NIM A735(2014)145–151
Kinematical focussing increases neutron intensity in a forward cone.
Licorne Facility at IPNO
MeV

## Slide 29: Kinematical focussing 1H(7Li,n)7Be
Two neutron groups
Strong forward focussing
In the laboratory
Kinematical focussing
Strong close to reaction threshold
E(7Li)=13.15 MeV
13.25
13.50
14.0
14.5
15.0
15.5
16.0
16.5

## Slide 30: „Big Four“ reactions for neutron production
 | D(d,n)3He | T(p,n)3He | T(d,n)4He | 7Li(p,n)7Be
Q-value(MeV) | 3.2689 | -0.7638 | 17.589 | -1.6442
Neutron emission yield at 0°
With
quasimonoenergetic range indicated by dashed lines
No monoenergetic neutrons in the
Gap between 7.7 – 13.2 MeV
R. Nolte, D.J. Thomas,
Metrologia 48 (2011) S263

## Slide 31: Monoenergetic neutron reference fields
D(d,n)3He
T(p,n)3He
T(d,n)4He
7Li(p,n)7Be
relative Yield
Y(0°) calculated for
T(d,n)4He:
rather isotropic
7Li(p,n)7Be:
production of keV neutrons at backward angles (reduced yield)
neutron emission angle (lab)
neutron emission angle (lab)
Parameters of reference fields (En,Y, target, beam properties)
see table 2 of
R. Nolte, D.J. Thomas, Metrologia 48 (2011) S263
En(0°)=
En(0°)=

## Slide 32: PTB neutron reference facility
neutron producing target
Ti(T), 7Li, …
air cooled, rotating target
Neutron reference fields are produced in open geometry without collimation
Very low room return due to large free space around source and detectors
Van der Graaff Ion accelerator for 1 – 4 MeV protons, deuterons with DC beam and pulsed beam t = 1-2ns,   1 MHz
Experiment: detector to be calibrated:
T. Kögler fission chambers

## Slide 33: PTB neutron reference facility
shadow cone
Characterisation of the neutron spectrum by using a pulsed beam and measurement of the neutron time-of-flight
Background of air-scattering and room-return neutrons from shadow cone measurement
Experiment: detector to be
calibrated
neutron producing target
Ti(T), 7Li, …
air cooled, rotating target

## Slide 34: Characterization of neutron producing targets
Time of flight spectrum of neutrons (En=1.2 MeV) from a Ti(T) target 0.853 mg/cm2
bombarded with protons Ep=2.042 MeV
„TARGET“ simulation shows effect of
time resolution of beam and detector
Tail in ToF spectrum
Tritium diffusion into the Ti backing
Target depth profile measured with a narrow 7Li(,)11B* resonance (cm 1.8 eV) at E= 814 keV (at 953 keV is the next resonance)
Detection of energetic -rays as a function of E
Tails show diffusion of the 7Li in the Ta backing and
corrosion after contact with air Li  Li(OH)
Lithium diffusion into the Ta backing
R. Nolte, D.J. Thomas, Metrologia 48 (2011) S263

## Slide 35: Neutron generators
D-D Generator 2H(2H,n)3He Q = 3.26 MeV
D-T- Generator 3H(2H,n)4He Q = 17.16 MeV
positive Q-value  only small deuteron accelerator required ED = 100…300 keV
Thick target yield 109 n/s (D-D) 1012 n/s (D-T)
D-T Generator of TU Dresden at HZDR has a high nominal yield 1012 n/s (D-T) up to 10 mA beam current
commercial neutron generators are available in many sizes

## Slide 36: D-T und D-D Fusion Reactions
D-T cross section is ca. 250 times larger than DD at E= 100 keV
At 95° (lab) the neutron spectrum is quasi monoenergetic even if a thick target is used.
Experimental data from EXFOR data base

## Slide 37: 3H(d,n)4He S-Factor
Removes the dominant Ecm dependence from the cross section  due to the Coulomb barrier penetration and de Broglie wavelength in the entrance channel
http://pntpm3.ulb.ac.be/Nacre/nacre.htm
3H(d,n)4He peaked at resonance in 5He at Ed = 107 keV (64 keV Ecm)

## Slide 38
Resonances in the unbound nucleus 5He
F.C. Barker, Phys. Rev. C56 (1997) 2646
http://www.tunl.duke.edu/nucldata/index.shtml

## Slide 39
A. Domula, DPG spring meeting, Bonn, 2010

## Slide 40: DT, DD neutron spectrum
Ed=2.682 MeV
Neutron time of flight spectrum of Ti(T) target
Background from reactions on target contaminants 12C(d,n0)13N, not easy to subtract
D(d,n)3He reaction on deuterium implanted in the Ti(T) target
blank Ti backing
Spectrum subtracted
„TARGET“ simulation
R. Nolte, D.J. Thomas, Metrologia 48 (2011) S263